## Slide 1: Sound Wave Inspection Systems

## Slide 2: Introducing Sonic V
Fifth generation of Acoustic Pulse Reflectometry technology

## Slide 3: Acoustic Pulse Reflectometry
Sonic V Adaptor
Specially formed acoustic pulses are propagated through the air enclosed by tube
Echoes generated by defects are recorded using cutting edge microphones
Powerful algorithms are identifying location, type and size of ID defects
Acoustic pulse injected in tube
Echo reflected from defect

## Slide 4: APR Signals
Wall Loss
pitting, erosion
Blockage
deposits, dents, welding material
Impulse
Reflection from a local blockage
t
Reflection from a
local wall loss
Reflection from a hole

## Slide 5: Hole
Signature of hole compared to reference and faultless signals

## Slide 6: Blockage
Blockage signal compared to reference and faultless signals

## Slide 7: Wall loss
Wall loss signatures near end of the tube compared to reference and faultless signals

## Slide 8: APR Advantages
ID defects detection
Extremely sensitive to holes and blockages/restrictions
Easy detection of ID wall losses (pitting, erosion)
Practical solution
Ultra-fast, non-invasive inspection/less than 10 seconds per tube
No need for inventory of consumable probes or standards
Easy operation with minimal training

## Slide 9: APR Limitations
No OD defect detection
No crack detection
Sensitive to cleanliness
  For leakage detection and blockage detection minimum dry-blowing of tubes in order to blow out dirt
  For full ID wall loss inspection all dirt / scaling should be removed

## Slide 10
Complete ID coverage of all types of tubes
U-bends, fin-fans, twisted, spiral wound tubes
Ferromagnetic and non-ferromagnetic metals, graphite and plastics
ID diameters from 6mm to 50mm
Up to 20 meters depending on defect size, tube configuration and type
Applicability

## Slide 11: Sonic V Hardware Features
Completely new, innovative design
Fits in a small backpack
Both, battery and electricity operated
Long battery life
  5+ hours on a single charge
  Battery hot swapping
No calibration tubes
No cables
Two cutting edge microphones
Touchscreen
Airline approved
Extremely fast

## Slide 12: Sonic V Software Features
Effortless mapping process
User friendly interface
Automatic session backup
Data upload directly from Sonic V

## Slide 13: Operation
Map and parameters setup
Data collection and Upload
Report
Get the job done in three simple steps

## Slide 14: Map and Parameters Setup
Effortless map creation
  Using photo, drawing or manually
  Automatic tube selection and ordering
Parameters required
  Length
  OD diameter
  Wall thickness
  Ambient temperature

## Slide 15: Data Collection and Upload
Hassle-free inspection
  All information displayed on LCD
  Easy navigation
  Bad measurement warnings
Upload data for analysis using built in tools
  Directly from the device via Wi-Fi
  Using USB thumb drive and dedicated software

## Slide 16: Report
Get the top quality final reports within max 24h
Analysis done by the most experienced analysts
Report designed according to industry standards

## Slide 17: Package Contents
Protective backpack
Two battery sets
Charger
Adaptors (6mm-50mm)
Windows/Linux/Android software for easy setup

## Slide 18: Industries
Oil & Gas (refineries, fuel processing)
Power generation utilities
Petrochemicals, chemicals
Food and beverage
Air conditioning (HVAC)
Pulp and paper
Tube cleaning QA

## Slide 19: Standards
ASTM international approved standard ASTM E2906 / E2906M – 13
  Standard Practice for Acoustic Pulse Reflectometry Examination of Tube Bundles
ASME standard
  2015 Boiler & Pressure Vessel codebook article 18, book V (five)

## Slide 20: Summary
Ultra-fast speed
  Significantly faster than conventional inspection techniques
  Less than 10 seconds per tube
Ease of use
  Single operator inspection
  Consistent, repeatable results
  Battery operated
  Mobility, whole system fits in a small backpack
Full coverage
  Any shape (u-bends, “S” shape, twisted)
  Any material (ferromagnetic, non-ferromagnetic)
  Up to 50mm ID

## Slide 21: Thank you
www.swis.ltd